|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Recreational Sports - Cal Adventures |
|  | Assembling/Disassembling/Repairing Ropes Course |
|  | General Precautions: Hard hats and eye protection must always be worn. The fall-protection equipment must be inspected and maintained according to Cal/OSHA guidelines and manufacturer’s recommendations. A rescue plan and equipment must be in place and operable prior to climbing tree. |
|  | Task | Hazards | Controls |
|  | Securing the perimeter of work area from bystanders. | None foreseen. |  |
|  | Fastening self into harness. | Pinching fingers. | Keep fingers away from the clamp area of carabineer. |
|  |  | Falling while attempting to step into the harness. | Hold onto a stable object for balance or solicit the help of other personnel. |
|  | 3. Securing the ladder against the tree. | Injury to self and others from losing control of the ladder. | See EH&S fact sheet on “Ladder Safety” for more information. |
|  | 4. Ascending/descending the ladder. | Unstable ladder. | See EH&S fact sheet on “Ladder Safety” for more information. |
|  |  | Falling. | Inspect tree, especially stable ladder, to ensure everything is secure. See EHS fact sheet on “Ladder Safety” for more information. |
|  | 5. Clipping the harness onto the gliding pulley system. | Pinching fingers. | Keep fingers away from clamp area of carabineer. |
|  | 6. Sitting back into harness. | Injury from the harness due to suspension. | Slowly sit back into harness. Stabilize body to minimize swinging in harness. |
|  | 7. Clipping the tote bucket onto the gliding pulley system. | Pinching fingers. | See above for more information. |
|  | 8. Gliding along pulley system. | Finger/hand injuries. | Keep fingers and hands clear of carabineer. Be careful of rope burn. |
|  |  | Injury to others. | Make sure every tool is secured to tote bucket by rope. Ensure that no one is underneath the work area. |
|  | 9. Performing task. | Injury from falling objects. | Wear a hard hat and eye protection. |
|  | Required Training: Using harness, fall protection | Required Personal Protective Equipment (PPE): Hard hat, eye protection, harness |
| Other Information: | See “Ladder Safety” Fact Sheet |
| Contributors: | Recreational Sports |
| Created: | June 2005 |
| JSA Library Number: | RS-CA-4 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |
|  | The development of Job Safety Analyses is a Balanced Scorecard initiative of the AVC-BAS Safety Committee, sponsored by the Associate Vice Chancellor-Business and Administrative Services (AVC-BAS) and the AVC-BAS Leadership Team ( http://bas.berkeley.edu/balancedscorecard |