This template is a Microsoft Word table – use MS Word’s online “Help” feature for instructions about how to add text and format tables.

|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Environment, Health & Safety – Chemical Waste |
|  | Opening Closing Drums with Bung Wrench |
|  | Task | Hazards | Controls |
|  | Removing bung cap with bung wrench. | Hand and finger injury. | Ensure bung wrench is properly engaged before applying pressure. Wear heavy gloves. |
|  |  | Injuries from pressurized drums. | Do not open bulging drums. Do not lean directly over the drum while opening. |
|  | Required Training: Familiarization with this JSA. | Required Personal Protective Equipment (PPE): Steel-toed boots, lab coat or tyvek suit, safety glasses, and cotton or leather gloves |
| Other Information: |  |
| Contributors: | Environment, Health & Safety |
| Created: | June 2005 |
| JSA Library Number: | EHS-1HM-4 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |