This template is a Microsoft Word table – use MS Word’s online “Help” feature for instructions about how to add text and format tables.

|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Environment, Health & Safety – Chemical Waste |
|  | Opening/Closing Drums with Air Wrench (Open-Head Drums) |
|  | Task | Hazards | Controls |
|  | Use air wrench to remove closure bolt. | Hand injuries. | Ensure air wrench is properly positioned on bolt head. |
|  |  | Slipping, tripping and falling. | Do not lay air line across high-traffic areas. Be aware of air line. Route it away from you. |
|  | 2. Remove lid ring. | Hand and finger injury (pinches). | Wear heavy gloves. |
|  | 3. Hand and finger injury (cuts). | Hand and finger injury (cuts). | Wear heavy gloves. |
|  | 4. Fill drum (Lab Pack). | Back or muscle strain. | Avoid long periods of repetitive motion (reaching into drum). Keep the drum flat on the base balance when reaching inside. |
|  | 5. Closing drum is reverse of tasks 1-3. | (See hazards 1-3). | (See controls 1-3). |
|  | Required Training: 1. Familiarization with air tools. 2. Familiarization with this JSA. | Required Personal Protective Equipment (PPE) Steel-toed boots, lab coat or tyvek suit, safety glasses, and cotton or leather gloves |
| Other Information: |  |
| Contributors: | Environment, Health & Safety |
| Created: | June 2005 |
| JSA Library Number: | EHS-1HM-2 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |