This template is a Microsoft Word table – use MS Word’s online “Help” feature for instructions about how to add text and format tables.

|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Environment, Health & Safety – Radioactive Waste |
|  | Determining the Contents of the Drum and Preparing for A Potential Spill |
|  | Task | Hazards | Controls |
|  | Examine the rim of the drum, lid, and sealing ring to be sure they will sit properly. | Pinch hand while handling parts. | Wear leather or similar gloves. Use care (don’t grab) while examining parts. |
|  |  | Cuts or abrasions from burrs on metal parts. | Wear leather or similar gloves. Keep your hands open (don’t grab) while examining parts. |
|  | 2. Place the lid on the drum, sit the ring, and tighten the bolt using a wrench. | Pinch hand while handling parts. | See 1a-1. |
|  |  | Cut abrasions from burrs on metal parts. | Use care and wear leather or similar gloves. |
|  |  | Abrasion or impact from tightening the bolt. | Position your body so the wrench can be easily turned. |
|  | 3. Attach the ring clamp for hard to sit rings, and torque into place by turning the handle. | Impact and pinch while positioning the ring clamp. | See 1a-1. Hold the clamp so the components don't slip over the threaded shaft. |
|  |  | Muscle strain from tightening the clamp. | Position your body so the clamp tightening handle can be easily turned. |
|  | 4. Secure and tighten the nut on the ring bolt using the pneumatic hammer drill. | Muscle strain from tightening the ring bolt. | Seat the pneumatic hammer drill properly on the nut. Position your body to stabilize the position of the hammer drill prior to pulling the trigger. |
|  | Required Training: 1. Use of the ring clamp positioning and tightening clamp. 2. Hazards associated with drum contents. | Required Personal Protective Equipment (PPE): Leather or similar gloves, safety glasses, steel toed shoes |
| Other Information: |  |
| Contributors: | Environment, Health and Safety |
| Created: | June 2005 |
| JSA Library Number: | EHS-2HM-2 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |