|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Environment, Health & Safety - Dock Leveler Operation |
|  | Task | Hazards | Controls |
|  | Open electric roll up door. | Potential injury from getting struck by the door as it rises | Stand back from rising door. Wait for door to fully rise. |
|  |  | Slipping, tripping, or falling | Always look and be aware of potential for slipping, tripping, or falling. |
|  | 2. Raise the dock leveler. | Injury from falling off dock or between dock and vehicle | Watch your step. Don’t walk onto tailgate of truck until dock leveler is in place. |
|  |  | Slipping from wet surface (ex.: rain) | Clean up if possible. If clean up is not possible, then use extreme care if walking on wet surface is necessary. |
|  |  | Potential fall from leveler as it is raised | Ensure dock leveler is clear before raising. |
|  |  | Risk of pinch to feet as leveler lowers to truck bed | Wear steel-toed safety boots. Stand back from dock leveler when in use. Do not walk onto leveler until completely level. |
|  | 3. Lower dock leveler. | Potential fall from leveler as it is raised | Ensure dock leveler is clear before raising. |
|  |  | Risk of pinch to feet as leveler lowers to truck bed | Wear steel-toed safety boots. Stand back from dock leveler when in use. Do not walk onto leveler until completely level. |
|  | 4. Lower electric roll up door. | Potential to be struck and/or fall by door as it lowers. | Stand back as door lowers. |
|  | Required Training: Hazard communication Saw operation | Required Personal Protective Equipment (PPE) Safety shoes Leather gloves Lab coat |
| Other Information: |  |
| Contributors: | HMF 1st Floor: EH&S Principal Technician Aaron Wilber |
| Created: | April 2003 |
| JSA Library Number: | EHS-1HM-7 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |
|  | The development of Job Safety Analyses is a Balanced Scorecard initiative of the AVC-BAS Safety Committee, sponsored by the Associate Vice Chancellor-Business and Administrative Services (AVC-BAS) and the AVC-BAS Leadership Team ( http://bas.berkeley.edu/balancedscorecard |