This template is a Microsoft Word table – use MS Word’s online “Help” feature for instructions about how to add text and format tables.

|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Environment, Health & Safety – Radioactive Waste |
|  | Moving A Loaded 55-Gallon Drum |
|  | Task | Hazards | Controls |
|  | Open the drum or container. | Pinch hand while handling bolt, ring, and lid. | Wear leather or similar gloves. Use care (don’t grab) while handling parts. |
|  |  | Cuts or abrasions from burrs on metal parts. | Wear leather or similar gloves. Keep your hands open (don’t grab) while handling parts. |
|  | 2. Unbolt the ring using a wrench. | Pinch hand while handling parts. | Wear leather or similar gloves. |
|  |  | Cut abrasions from burrs on metal parts. | Use care and wear leather or similar gloves. |
|  |  | Abrasion or impact from loosening the bolt. | Position your body so the wrench can be easily turned. |
|  | 3. Unlatch the bolt and loosen the ring by stretching it before removing. | Impact and pinch while removing the ring. | Wear leather or similar gloves. Hold the ring so the components and hands don't get caught on the rim of the lid. |
|  |  | Muscle strain from loosening the ring. | Position your body so the ring can be easily removed. |
|  | Required Training: 1. Use of the ring clamp. 2. Hazards associated with drum contents. | Required Personal Protective Equipment (PPE): Leather or similar gloves, safety glasses, steel-toed shoes |
| Other Information: |  |
| Contributors: | Environment, Health and Safety |
| Created: | June 2005 |
| JSA Library Number: | EHS-2HM-6 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |