|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Facilities Services |  |  |
|  | Maintenance of Fire Alarms, Panels, and Sensors |
|  | Task | Hazards | Controls |
|  | Preparing work area | Injuries to passersby and bystanders | Isolate work area with barricades, caution tape, and/or on-site assistant |
|  |  | False alarm response; client anxiety/irritation/panic; disruption of campus business | Phone UCPD and notify building clients; schedule work appropriately |
|  | 2. Using ladders and lifts | Falls, slips, electrical hazards | Refer to ladder safety and aerial lift JSAs. |
|  | 3. Working in sub-ceilings, cramped spaces, custodial closets, machine rooms | Muscle strain, repetitive stress injuries | Stretching, frequent breaks, adequate hydration, alternate tasks with team partner |
|  |  | Heat stress | Frequent breaks, adequate hydration, alternate tasks with team partner |
|  |  | Head and/or eye injuries from falling or flying debris, dust inhalation | Protect head and eyes with hard hat and safety glasses; wear dust mask. |
|  |  | Hand and finger injuries from pinch points | Protect hands with gloves; avoid pinch points and moving machinery parts. |
|  |  | Skin/eye irritation from dirt and chemicals | Wear safety glasses and long-sleeved shirt. |
|  |  | Tripping hazards from cables and extension cords | Practice careful housekeeping; maintain awareness of location of equipment and tools. |
|  | 4. Repairing, replacing, or maintaining fire alarms, panels, or sensors | Electrical shock | Assess environment for water or damaged wiring/connectors before starting work; evaluate condition/age of building and consult written procedures (confidential to department) for that building before starting work. |
|  | 5. Testing horns | Hearing damage to self and others | Wear ear plugs; notify building clients and UCPD prior to tests. |
|  | Required Training: Ladder safety Aerial lift training Electrical safety Departmental building-specific alarm maintenance procedures | Required Personal Protective Equipment (PPE) Safety glasses Dust mask Hard hat Gloves Ear plugs |
| Other Information: |  |
| Contributors: | Senior EH&S Technician Jim Ostdick; Fire Alarm Inspection & Testing Supervisor Karen Lobo; Fire Alarm Technician Hadi Kamkar |
| Created: | July 2003 |
| JSA Library Number: | FS-FIRE-212 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |
|  | The development of Job Safety Analyses is a Balanced Scorecard initiative of the AVC-BAS Safety Committee, sponsored by the Associate Vice Chancellor-Business and Administrative Services (AVC-BAS) and the AVC-BAS Leadership Team ( http://bas.berkeley.edu/balancedscorecard |