|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Facilities Services |  |  |
|  | Operating a 12-inch Chop Saw |
|  | Task | Hazards | Controls |
|  | Check saw blade for sharpness, obstructions, properly functioning guard | Loose, obstructed, or dull blades or guards create pinching hazards | Adjust and tighten blades and guards Avoid contact with blade teeth. |
|  | 2. Align materials flat on table and flush to the back of table | Pinching fingers or hand | Keep fingers and hands away from pinch points. |
|  | 3. Start and operate saw. | Cutting fingers and hands | Keep fingers and hands away from blade. |
|  |  | Flying sawdust | Wear safety glasses or face shield. |
|  | Required Training: 1. Operation of chop saw | Required Personal Protective Equipment (PPE) Safety glasses Face shield |
| Other Information: |  |
| Contributors: | Senior EH&S Technician Jim Ostdick; Lead Carpenter Louis Mandrigues |
| Created: | March 2003 |
| JSA Library Number: | FS-CARP-100 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |
|  | The development of Job Safety Analyses is a Balanced Scorecard initiative of the AVC-BAS Safety Committee, sponsored by the Associate Vice Chancellor-Business and Administrative Services (AVC-BAS) and the AVC-BAS Leadership Team ( http://bas.berkeley.edu/balancedscorecard |