|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Facilities Services |  |  |
|  | Operating a 14-inch Radial Arm Saw |
|  | Task | Hazards | Controls |
|  | Prepare work area. | Inhalation of sawdust | Turn on exhaust fan |
|  |  | Sawdust in eyes | Wear safety glasses or face shield |
|  | 2. Check guard and saw blade. | Pinching/cutting fingers and hands | Avoid pinch points and sharp edges; wear gloves if necessary. |
|  | 3. Align material on table against fence and in front of saw blade. | Pinching fingers and hands | Avoid pinch points between material and table/fence. |
|  | 4. Turn on saw. | Sawdust in eyes | Wear safety glasses or face shield. |
|  |  | Cutting fingers | Keep fingers and hands well away from saw blade. |
|  | 5. Cut material. | Cutting fingers | Keep fingers and hands well away from saw blade. |
|  |  | Cutting fingers, hands, or other body parts | Stand well to the right side of saw blade when cutting material, keep fingers and hands away from the blade; allow the blade, guard, table, and fence to do the work of cutting and gripping the material. |
|  |  | Sawdust in eyes | Wear safety glasses or face shield. |
|  | Required Training: 1. Operation of radial arm saw | Required Personal Protective Equipment (PPE) Safety glasses or face shield Gloves |
| Other Information: |  |
| Contributors: | Senior EH&S Technician Jim Ostdick; Lead Carpenter Louis Mandrigues |
| Created: | March 2003 |
| JSA Library Number: | FS-CARP-161 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |
|  | The development of Job Safety Analyses is a Balanced Scorecard initiative of the AVC-BAS Safety Committee, sponsored by the Associate Vice Chancellor-Business and Administrative Services (AVC-BAS) and the AVC-BAS Leadership Team ( http://bas.berkeley.edu/balancedscorecard |