|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Facilities Services |  |  |
|  | Operating an Electric Spot Welder |
|  | Task | Hazards | Controls |
|  | Align material. | Cutting hand | Wear leather gloves. Deburr test strips. Do not slide hands along edges. |
|  |  | Pinching hand between welding tips | Wear gloves. Keep fingers from pinch point |
|  | 2. Depress foot pedal to activate welder. | Cutting hand | Wear leather gloves. |
|  |  | Pinching hand between welding tips | Wear gloves. Keep fingers from pinch point. |
|  |  | Burning hands | Wear gloves. |
|  |  | Flying sparks burning eyes | Wear safety glasses. |
|  |  | Muscle strain | Position body to support material, and get assistance when necessary. |
|  | 3. Remove material. | Cutting hand | Wear leather gloves. Deburr test strips. Do not slide hands along edges. |
|  | Required Training: 1. Operation of electric spot welder | Required Personal Protective Equipment (PPE) Gloves Safety glasses |
| Other Information: |  |
| Contributors: | Senior EH&S Technician Jim Ostdick; Sheet Metal Worker Greg Rasmussen |
| Created: | November 2002 |
| JSA Library Number: | FS-SMETAL-15 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |
|  | The development of Job Safety Analyses is a Balanced Scorecard initiative of the AVC-BAS Safety Committee, sponsored by the Associate Vice Chancellor-Business and Administrative Services (AVC-BAS) and the AVC-BAS Leadership Team ( http://bas.berkeley.edu/balancedscorecard |