|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Facilities Services |  |  |
|  | Operating a Vertical Saw |
|  | Task | Hazards | Controls |
|  | Align material on saw platform. | Muscle strain | Position body to maintain balance. Maximize use of legs. Avoid twisting and overextending. |
|  | 2. Operate saw to make cut. | Lacerations to hand | Keep hands away from saw carriage. |
|  |  | Sawdust debris in eyes | Wear safety glasses and face shield. Use vacuum attachment to remove sawdust. |
|  | Required Training: 1. Operation of vertical saw and vacuum system | Required Personal Protective Equipment (PPE) Safety glasses Face shield Non-skid shoes |
| Other Information: |  |
| Contributors: | Senior EH&S Technician Jim Ostdick; Glazier Rudy Fuentes |
| Created: | January 2003 |
| JSA Library Number: | FS-PAINT-5 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |
|  | The development of Job Safety Analyses is a Balanced Scorecard initiative of the AVC-BAS Safety Committee, sponsored by the Associate Vice Chancellor-Business and Administrative Services (AVC-BAS) and the AVC-BAS Leadership Team ( http://bas.berkeley.edu/balancedscorecard |