|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | UC Printing Services |
|  | Operation of the Interlake Handstitch Machine |
|  | Task | Hazards | Controls |
|  | Set up to hand saddle a wire booklet. | Pinch point under stitch head. | Make sure safety guard is in place. |
|  | 2. Set up for back gauge on flat wire. | Scrape knuckles. | Use proper tool to loosen bolts. |
|  | 3. Change wire spool. | Pricks from wire. | Use proper tool to feed wire into stitch head. |
|  | 4. Run hand stitch. | Pinch point. | Make sure safety guard is in place. |
|  | Required Training: | Required Personal Protective Equipment (PPE) |
| Other Information: |  |
| Contributors: | Theresa Acree, UC Printing Services. |
| Created: | January 2006 |
| JSA Library Number: | UCPS-06 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |