|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | UC Printing Services |
|  | Operation of the Horizon BQ240 Binder |
|  | Task | Hazards | Controls |
|  | Set up spine width. | Pinch points at clamp. | Start in the DOWN position. Measure for spine in UP position. Set book with clamp only – not hands. |
|  | 2. Set up grind for spine width. | Injury to hands from moving circular grind blade. | Set up spine width only when machine STOP switch is engaged. Safety guard must be down to re-engage the ON switch. Adjust with safety guard in open position. |
|  | 3. Adding glue chips to glue pot. | Skin burns from glue at 200°. | Pour chips into pot slowly and at close range. Do not reach into pot. |
|  | 4. Adjust glue stream. | Skin burns. | Use proper tool to adjust scraper on wheel. |
|  | Required Training: | Required Personal Protective Equipment (PPE) |
| Other Information: |  |
| Contributors: | Theresa Acree, UC Printing Services. |
| Created: | January 2006 |
| JSA Library Number: | UCPS-13 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |