|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | UC Printing Services |
|  | Operation of the Bell & Howell Inserter |
|  | Task | Hazards | Controls |
|  | Set up pocket feed. | Pinch point at swing arm. | Use two-button jog to set and make adjustments in the STOP position. |
|  | 2. Set up timing on chain. | Pinch point at moving chain. | Use two-button jog to set timing and make adjustments in the STOP position. |
|  | 3. Set up delivery. | Pinch point with rollers and belts. | Set delivery in the STOP position. |
|  | Required Training: | Required Personal Protective Equipment (PPE) |
| Other Information: |  |
| Contributors: | Theresa Acree, UC Printing Services. |
| Created: | January 2006 |
| JSA Library Number: | UCPS-07 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |