|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | UC Printing Services |
|  | Operation of the Kirk Rudy Cheshire Labeler |
|  | Task | Hazards | Controls |
|  | Set up feeder. | Pinch point at moving shuttle. | Set up in STOP position only with STOP switch engaged. |
|  | 2. Set up glue rollers and cam. | Hand injury from moving rollers. | Set up, clean, and remove jammed labels in STOP position only. |
|  | 3. Set up label feed. | Hand injury from sharp knives. | Set up and adjust in the STOP position only. |
|  | 4. Delivery table. | Pinch points at moving belts. | Set up and adjust in the STOP position only. |
|  | Required Training: | Required Personal Protective Equipment (PPE) |
| Other Information: |  |
| Contributors: | Theresa Acree, UC Printing Services. |
| Created: | January 2006 |
| JSA Library Number: | UCPS-11 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |