|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | UC Printing Services |
|  | Operation of the Muller Martini 335 Stitcher |
|  | Task | Hazards | Controls |
|  | Set trim size three-knife. | Cuts from exposed blades. | Do not reach under blades and use pliers to remove any paper jams under knives. Make sure stop switch is engaged when removing jams. |
|  | 2. Set timing in three-knife. | Hand injury when using tool to loosen brake. | Use consistent force with tool in position so that when brake is released, motion does not slam down on guards. |
|  | 3. Set timing chain. | Hand injury when using tool to loosen bolts. Back injury from twisting and squatting. | Position hands and body to the side of the machine that is most comfortable for the size of the person performing task. Keep chain lubricated for ease of movement. |
|  | 4. Set stitch heads. | Pricked finger from wire. Pinch points under stitch heads cycling down. | Use wire cutters to move wire into head. Make all adjustments with two-hand jog switch and stop switch engaged with cover open. |
|  | 5. Running the machine. | All hazards described above. Injuries from moving chain. | Make all adjustments with two-hand jog switch and stop switch engaged with cover open. Do not reach into moving chain. |
|  | 6. Change knife. | Hand injury while using tools to manipulate bolts. | Tools of the proper length should be provided. |
|  |  | Hand injury from sharp knives. | Use knife guards. |
|  |  | Pinch points when removing and replacing clamps. | Remove clamps with knife carriage in up position. |
|  |  | Back injury while removing and replacing front clamp. | Move delivery table away from machine sos body can stand at or near work area. |
|  | 7. Changing feeder head position. | Smashing injury to hand when pushing carrier (feeder will sway). | Move carrier slowly or ask for help. |
|  | Required Training: | Required Personal Protective Equipment (PPE) |
| Other Information: |  |
| Contributors: | Theresa Acree, UC Printing Services. |
| Created: | January 2006 |
| JSA Library Number: | UCPS-02 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |