|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Recreational Sports - Maintenance |
|  | Using hand-operated Power Tools |
|  | General Precautions: Eye protection must always be worn. |
|  | Task | Hazards | Controls |
|  | Check condition of blade, if applicable. | Lacerations | Avoid contact with blade teeth. Be sure the tool is unplugged. |
|  | 2. Check that guard is in working condition and in the proper position, if applicable. | Lacerations | Avoid contact with blade teeth. Be sure the tool is unplugged. |
|  | 3. Plug in the power tool. | Injuries from tool starting due to being in “on” position | Ensure tool is in the “off” position before plugging it in. |
|  |  | Potential electrocution from cord being in poor condition | Inspect integrity of cord before plugging in. If in poor condition, do not use the tool until the cord has been repaired. |
|  | 4. Operate the power tool. | Lacerations and other injuries | Always wear safety goggles. Evaluate surrounding before turning power tool on and be aware of others. Don’t wear loose clothing. Secure material being operated on. |
|  | 5. Unplug the power tool. | Lacerations | Ensure tool is in the “off” position before unplugging it. |
|  | 6. Changing blade/bit/other tool parts. | Lacerations | Ensure tool is unplugged before changing any part of the tool. |
|  | Required Training: Operation of the tool | Required Personal Protective Equipment (PPE) Gloves, eye protection, and mask when necessary. |
| Other Information: |  |
| Contributors: | Department of Recreational Sports |
| Created: | June 2004 |
| JSA Library Number: | RS-Maint-06 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |