|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | UC Printing Services |
|  | Operation of the Hanagata Shrinkwrap |
|  | Task | Hazards | Controls |
|  | Place roll of shrink film onto feed carriage. | Shoulder and back injury from improper lifting over head. | Stand on platforms provided in shop. |
|  | 2. Feed film as indicated by numbers through rollers. | Pricking by feeder pins. | Perform task only with stop switch engaged and feeder rollers open by lever. |
|  | 3. Thread film onto film feed rollers and hot knife. | Pinch points. Hand injury. | Do not reach into rollers when engaging feed control. Do not put hands into knife area when cutting film. Remove test bag only after the knife has come to a complete stop. |
|  | 4. Advance film to tie off onto waste roll. | Hand injury from heated clamp. | Do not reach into the clamp area until the knife has come to a complete stop. |
|  | Required Training: | Required Personal Protective Equipment (PPE) |
| Other Information: |  |
| Contributors: | Theresa Acree, UC Printing Services. |
| Created: | January 2006 |
| JSA Library Number: | UCPS-08 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |