|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | UC Printing Services |
|  | Operation of the Baler System Waste Evacuation |
|  | Task | Hazards | Controls |
|  | Tying off a full bale. | Hand injury from sharp ends of wire. | Gloves are available and recommended. |
|  |  | Pinch point when twisting wire. | Gloves are available and recommended. |
|  | 2. Releasing a full bale. | Possible back strain when pushing bale over to skid. | Ask for available help to push bale over to pallet. |
|  | 3. Removing full bale, closing door, and restarting. | Pinch and smashing injuries when closing the door. | One person operation to restart hydraulic “Door Close” action. |
|  | 4. Checking system for jammed stock. | Injury to person in hopper. | Last resort to clear jam, use “Lock Out/Tag Operation” in which key is taken out and placed in the pocket of the person performing the task. |
|  | 5. Clean up and sweep floor. | Injury if hand or body part is pulled near air vacuum. | Use broom only – DO NOT reach near floor shoot. |
|  | Required Training: | Required Personal Protective Equipment (PPE) |
| Other Information: |  |
| Contributors: | Theresa Acree, UC Printing Services. |
| Created: | January 2006 |
| JSA Library Number: | UCPS-09 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |