This template is a Microsoft Word table – use MS Word’s online “Help” feature for instructions about how to add text and format tables.

|  | Job Safety Analysis |
| --- | --- |
|  | Safety Information for the University of California, Berkeley |  |
|  | Environment, Health & Safety – Radioactive Waste |
|  | Segregating Waste |
|  | Task | Hazards | Controls |
|  | Opening the drum or container. | Abrasions from the drum and muscle strains. | See the JSAs on opening and closing the drums. |
|  | 2. Segregating the containers according to the isotope and waste categories. | Cuts from sharps such as broken glass containers. | Wear gloves. Lift from the corner of the bag and examine for breakage and other sharps. |
|  |  | Radiation exposure due to leaking bags. | Lift from the corner of the bag from the opening edge and be careful not to spill contents. |
|  | 3. Weekly monitoring of radioactivity at each drum. | Potential radiation exposure due to unforeseen release of materials. | Use the radiation detector following procedures associated with use of the monitor. |
|  | Required Training: RP-20 Handling and Disposal of Radioactive Waste. RWI-2 Monitoring and Surveys. RWI-5: Decay Processing. RWI-9: Waste Pick-Up Procedure. RW1-10: Discrepant Waste Handling. RWI-60: Waste Characterization. Spill Response Procedures. | Required Personal Protective Equipment (PPE): Dosimetry, lab coat, safety glasses, steel-toed shoes |
| Other Information: | See JSA’s on opening and closing drums |
| Contributors: | Environment, Health and Safety |
| Created: | June 2005 |
| JSA Library Number: | EHS-2HM-8 |  |  |
|  | For more information about this JSA, contact the Office of Environment, Health and Safety at UC Berkeley, 317 University Hall #1150, Berkeley, CA 94720-1150 (510) 642-3073 ( http://www.ehs.berkeley.edu |